## Slide 1: Popcorn Linux: Compiler & OS Support for Execution Migration in Heterogeneous ISA Environments
Pierre Olivier, Sang-Hoon Kim
Systems Software Research Group
Virginia Tech
polivier@vt.edu, sanghoon@vt.edu

## Slide 2: Context: Instruction Set Architecture (ISA) Heterogeneity in the datacenter
Each image is copyright of the respective company or manufacturer. Images used here for educational purposes.
Notes: Multiple OS-capable ISAs, machines with different performances and power consumption profiles according to applications and part of applications
- How to leverage this? How can we have these ISAs working together? What is the programming model (can I run legacy code)

## Slide 3: Popcorn Linux Project
cpu3
krn1
cpu1
cpu2
krn0
cpu0
op environm
op environm
application
application
ISA A
ISA B
cpu1
cpu2
krn0
cpu0
cpu3
krn1
single operating environment
application
ISA A
ISA B
cpu1
cpu2
Kernel 0
cpu0
cpu3
Kernel 1
single operating environment
application
X86-64
specific code
ARM64
specific code
musl libc
GNU
popcornlinux.org
Sources
(unmodified)
Multi-ISA
Compiler
Compiler + kernel + runtime enabling native runtime migration of applications/threads across ISAs
  Transform architecture specific state (stack and registers) at runtime
    Support from compiler
  Transfer address space
    In-kernel distributed shared memory
Ethernet, Infiniband, etc.
Notes: Popcorn ecosystem: compiler, OS + runtime to enable application and thread migration across CPUs of different instruction set architectures
Takes unmodified application sources and compile them into multi-ISA binaries (instrumented and ready for migration)
Run on machines with CPUs of different ISAs, linked through some interconnect, and communicating at the OS level
  Distributed OS providing a unified operating env. based on Linux and provide basic communication and control primitives for migration
  User space runtime actually performs the translation upon migration
Migration is:
  Transform arch specific state (mostly stack) using metadata from the compiler
  Transfer on-demand the rest of the address space

## Slide 4: Motivation
Smart consolidation, load balancing for performance & energy gains
ISA/Machine affinity:
  Program phases illustration: PARSEC blackscholes native input
96 cores @2Ghz
6 cores @3.2Ghz
Notes: Talk about sequential and parallel phases:
  Seq: one core at 100% (not only IO)
  Parallel: all cores
Assuming a zero-cost migration time:
  Executing the right phase on the right machine would yield:
    32% execution time reduction compared to an only Xeon execution
    63% execution time reduction / 76% energy consumption reduction compared to an only Cavium execution.

## Slide 5: Outline
Compiler/toolchain support for multi-ISA binaries
OS support for heterogeneous migration
Evaluation, ongoing and future work
Conclusion

## Slide 6: Outline
Compiler/toolchain support for multi-ISA binaries
OS support for heterogeneous migration
Evaluation, ongoing and future work
Conclusion

## Slide 7: Popcorn Compiler Framework: Compiler Support for Heterogeneous-ISA Platforms
Pierre Olivier (polivier@vt.edu) Postdoctoral Associate
Work done by Robert Lyerly (rlyerly@vt.edu)
Notes: Credits to Rob

## Slide 8: Introduction
Goal: seamlessly run shared-memory/compiled applications across heterogeneous-ISA CPUs: no effort for the programmer
  Programmability and legacy support
    Use well-understood, high-performance languages like C/C++
      Compatible with legacy POSIX applications
    No manual application refactoring or partitioning of code across ISAs
  Manageability
    Enable system software to decide where to run applications
    Transparently leverage performance/energy benefits from diverse processors
Notes: For programmability reasons we focus on application written using the classical shared memory programming model
  Popular languages C C++
  No effort from the programmer to redesign the application or partition it across ISAs
Manageability: ecosystem enable automatic migration/distribution decisions without any explicit input from the programmer to leverage the benefits brought by heterogeneous environement

## Slide 9: Current Approaches
Message Passing Interface (MPI)
Complex code development/refactoring
ISA Virtualization
Managed languages, e.g., Java
  Rewrite application from scratch
  Performance overheads
Dynamic binary translation, e.g., QEMU
  Run unmodified binaries
  Order of magnitude slowdown
Notes: Message passing interface:
Significant developer effort
    Redesign entire application for legacy code
    Manual data movement
Virtualization
Managed languages - compile source code to intermediate representation, interpret by language VM on each ISA
  VM virtualizes ISA, can automate some data transfers
  Rewrite in new language – legacy not supported
  Significant performance overheads
    VM tasks, e.g., garbage collection
    Interpreter/JIT compiler overheads
    Data transfers are slow
System emulation – lift ISA-specific machine code to IR, re-compile down to host ISA

## Slide 10: Multi-ISA Binaries
Popcorn Compiler Toolchain builds multi-ISA binaries
  Create mostly-common virtual address space
    Valid across all ISAs
  Instrument generated code with migration points
  Insert translation metadata
    Used by runtime to dynamically transform thread execution state (stack, registers) between ISA-specific formats at migration time
C/C++ Source
Data
x86-64 Code
Transform Metadata
Popcorn Toolchain
Post-Processing
Link
Compile
Data
Transform Metadata
ARM64 Code
Notes: Popcorn Toolchain creates two binaries with minimal architecture specific differences: content of the code section
  For the rest (data): assume little endian and same size for primitive types
  Layout each symbol at the same address in the virtual address space to maintain reference validity across migration
Mostly-common address space solves almost all issues related to references. The exception is pointers to the stack, which are a nuisance. There’s two ways to handle them:
Venkat – align stack objects (whose addresses are taken) at identical stack slots across all ISA-specific stack formats. Very complete but highly invasive inside the compiler.
Me – at runtime, update references to stack objects to point to their relocated address. See next slide for more information on relocation costs.
My approach can lead to problems when passing references to stack objects to other threads, but this is generally considered an anti-pattern. There are a few places where this is valid, e.g., OpenMP shared variables, and I’m working on a possible solution.

## Slide 11: Multi-ISA Binaries
Minimize costs of migrating threads between ISAs
  Reification – cost of changing the binary representation to match what’s supported by the ISA
    Data: no cost, assume little-endian & equal sizes for primitive types
    Code: cost incurred offline – compiler generates code for each ISA
  Relocation – cost of moving data to different addresses
    Cost of copying memory between different addresses
    Cost of updating references (e.g., pointers) to those binary objects
Notes: This is a little more about the fundamental underpinnings on migration & its costs. This is probably too low-level for a presentation, but is in here for informational purposes.
x86-64 is strictly little-endian, but PowerPC & ARM64 are bi-endian.
Reification of data: there is a cost if you look to more extravagant types like IEEE quad-precision (128-bit) floating point. Some architectures support it, some don’t (and require software emulation). SIMD is another pain point. We disallow these types for now.

## Slide 12: Popcorn Compiler Toolchain
Built on top of clang/LLVM
  clang/LLVM 3.7.1, GNU gold 2.27 (~8k LoC)
  Virtual address space alignment tool (~1.5k LoC)
  State transformation/migration libraries (~4.5k LoC)
Notes: Modify clang/LLVM to emit multi-ISA binaries
  Lower application source into LLVM IR
    Insert migration points at function entry/exit (library function call)
  Analyze and instrument LLVM IR
    Run liveness analysis to determine which program variables are alive at potential transformation sites, i.e., all function call sites
    Adjust linkage of global variables & add symbol names so alignment tool can adjust layout
    Because we use single set of IR, can guarantee implementations are semantically equivalent, i.e. isomorphic
  In back-ends
    Record where live values are allocated in function activation, i.e., registers or stack slots
      Stack transformation runtime uses this metadata to transform stack
    Record frame unwinding metadata
      Similar to DWARF, but MUCH faster
Customized linking & post-processing creates uniform virtual memory space, adds stack transformation metadata to binaries

## Slide 13: Code Generation
…
C/C++
ISA-Agnostic LLVM IR
ISA-specific Machine Code
Track live values at the IR level
Record where live values are allocated, e.g “i” stored in %rbx
Notes: The LLVM toolchain
Clang – “C language frontend” – consumes C/C++ and emits LLVM IR
LLVM middle-end – language & architecture-agnostic optimizer – consumes LLVM IR and emits LLVM IR
LLVM back-end – code generation (e.g., instruction selection, register allocation) for each ISA – consumes LLVM IR and emits machine code
We track live values in the IR using the “stackmap” intrinsic (https://llvm.org/docs/StackMaps.html). We add live values as an argument to the stack map, and during the code generation (LLVM backend) phase each ISA’s backend records where the IR-level value is allocated for each ISA.
LLVM’s bitcode/IR is *mostly* ISA-agnostic because some ISA-specific operations get exposed in the IR, e.g., atomic operations, built-ins (hardware transactional memory functionality)

## Slide 14: Linking & Post-Processing
Generate linker script to align symbols across compilations for all ISAs
Post-process metadata from all compilations to clean and prepare for runtime state transformation
Notes: Post-process = rearrange LLVM’s stackmap section into my own sections.

## Slide 15: Migrating Between Architectures
Insert migration points into code
  Can only transform stack at equivalence points
    Direct mapping of execution state between ISA-specific formats
  Scheduler cannot migrate threads at arbitrary points, must signal threads to initiate migration process
No
Migrate thread?
Scheduler
void foo() {
migration_check();
… (execute foo) …
migration_check();
}
Thread
Yes
Transform execution state & migrate

## Slide 16: Migrating Between Architectures
Migration procedure:
  Transform stack & register set between ISA-specific formats
    Rewrite all open function activations from top to bottom
  Pass transformed state to OS thread migration service
  Thread bootstraps in well-known program location on destination processor & resumes at same location
Notes: Stack transformation
  Read the thread’s register set & attach to the stack
  Unwind the stack to find live function calls & calculate size for new stack
  Transform each frame between ISA-specific formats, i.e. copy live values to the appropriate locations
Thread migration service: __sched_setaffinity_popcorn system call
  OS copies PC, SP & FBP between ISA-specific equivalents (heterogeneous continuation)
Resumes in well-known location, fixes up floating-point registers (kernel doesn’t want to touch them)

## Slide 17: State Transformation
Source
Destination
Function: baz
Call site: 10
Call frame size: 32 bytes
Return address: 0x410548
Function: baz
Call site: 10
Call frame size: 48 bytes
Return address: 0x410532
Top of Stack
Function: bar
Call site: 37
Call frame size: 16 bytes
Return address: 0x410204
Function: bar
Call site: 37
Call frame size: 32 bytes
Return address: 0x410198
Function: foo
Call site: 193
Call frame size: 32 bytes
Return address: 0x412820
Function: foo
Call site: 193
Call frame size: 40 bytes
Return address: 0x412700
Notes: 1st phase of runtime: read the thread’s current stack, which lets us find the open function activations & their associated metadata entries. We can then calculate the size of the transformed stack from their metadata entries.

## Slide 18: State Transformation
Function: bar
Call site: 37
Call frame size: 32 bytes
Return address: 0x410198
Function: foo
Call site: 193
Call frame size: 40 bytes
Return address: 0x412700
Notes: The runtime handles pointers to stack variables as well:
The compiler generates enough type information to tell the runtime whether a live value is a pointer
When copying a pointer between the source & destination activations, the runtime checks if it points to within the stack’s bounds
  If so, the runtime records a “fixup”, meaning that the pointer needs to be reified after the pointed-to data has been relocated to the transformed stack
When copying stack-allocated data from source to destination, the runtime checks if any fixups point to the data on the source stack. If so, the pointer is reified on the destination stack

## Slide 19: State Transformation
How fast is state transformation?
Notes: State transformation latency for all migration points across several NPB applications
  Graph shows minimum, average, maximum latencies

## Slide 20: Summary
Compiler generates multi-ISA binaries
  Lower source to ISA-agnostic LLVM IR
    Instrument with migration points
  Lower single set of IR to multiple ISAs
    Track where live values are allocated for each ISA
    Supports a number of architectures (not just ARM & x86)
  Align binaries & add transformation metadata
Runtime migration
  Coordinate with scheduler to migrate threads
    Attach to thread’s registers & stack, rewrite in its entirety

## Slide 21: Outline
Compiler/toolchain support for multi-ISA binaries
OS support for heterogeneous migration
Evaluation, ongoing and future work
Conclusion

## Slide 22: OS Support for Heterogeneous Migration
Sang-Hoon Kim (sanghoon@vt.edu)
Postdoctoral Associate

## Slide 23: On the OS side …
Migrate threads
Provide consistent memory

## Slide 24: Thread migration
Equivalent to perform the context switch across machines
At origin: Save the execution context
  The user-space library provides the register set
  thread_struct + mm_struct
At remote: Restore the context on a thread
  Fork a kernel thread, and downgrade it to a user thread
  Construct mm_struct and associate it with the thread
  Update pt_regs and thread_struct
  Return from the kernel space
   Resume execution as if returned from system call
Exec.
contexts
Exec.
contexts
Origin
Remote

## Slide 25: Memory consistency protocol
Provide consistent memory to distributed threads
VMA (vm_area_struct)
  Metadata for pages in a range of address space
  E.g., types, permission, backing files, offset in files, …
Page (page)
  Data

## Slide 26: Memory consistency protocol VMA
VMA
Map
Kernel 2
Kernel 1
Single System Image
Original thread
Remote thread
VMA
Map
str x1, [sp,#0xbeef]
Page fault at sp + 0xbeef
send page containing sp + 0xbeef
Migrate to ARM
.text (x86)
.text (ARM)
Page fault at @str
Notes: When we decide to migrate the thread, kernel 1 tells kernel 2 to set up OS-side data structures
The user thread is migrated by the kernels (it goes to sleep on kernel 1 and is re-instantiated on kernel 2), and as it begins fetching instructions, kernel 2 maps the ISA-specific machine code into memory
  The OS knows that it’s fetching instructions from a code page by permission bits (executable, readable), so rather than migrating the page from kernel 1 it loads the page from disk
The thread starts accessing data and causes a page fault because the page it tries to access is not mapped into memory
  str (store register to memory), x1 is an integer register, [sp, #0xbeef] means the address generated by adding 0xbeef to the stack pointer register
Kernel 2 realizes that the thread is in the heterogeneous container, so at the page fault it asks kernel 1 if it has the page needed by the thread
Kernel 1 unmaps the page and sends it to kernel 2, who maps it into the thread’s address space and resumes the thread’s execution

## Slide 27: Memory consistency protocol Page
Centralized for the implementation feasibility
  Track the ownership for each page at the origin
  Remote threads request missing pages to the origin
  The origin handles the requests accordingly
Model the simple RMI cache coherent protocol
  Read-Modify Invalidate
  Read replicates a page
  Write gets exclusive access to the page
    Invalidates the page from other nodes
Local
Shared
Exclusive
Read
Write
Read
Write
Read
Write

## Slide 28: Memory consistency protocol Read
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Origin
Remote 1
Remote 2
Read
R
RW

## Slide 29: Memory consistency protocol Read
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Origin
Remote 1
Remote 2
Read
Read
R
Read
RW

## Slide 30: Memory consistency protocol Write
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Origin
Remote 1
Remote 2
Write
R
RW

## Slide 31: Memory consistency protocol Write
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Origin
Remote 1
Remote 2
Write
Invalidate
R
RW
Grant

## Slide 32: Memory consistency protocol In reality …
Page faults are inherently concurrent
  Each thread can raise a page fault
  Multiple faults for different pages
  Multiple faults for a page
In addition, faults can be happened simultaneously at the origin and remotes

## Slide 33: Memory consistency protocol In reality …
Current optimistic fault handling complicates ownership tracking
  Threads independently prepare faulty pages
  Serialized by PTE spinlock for PTE fixup
  May discard the prepared page if other already fixed up the PTE
  Remote fetch updates the ownership status at the origin
  Cannot just discard the page fetched from the origin…
Locking gets more complicated
  Cannot hold PTE spinlocks while fetching pages over interconnect
  Different PTE lock granularity for architectures and configurations

## Slide 34: Fault coalescing
Track outstanding fault handlings
Merge the same type of faults to the same page
The first thread staging a fault for a page becomes the leader
The leader executes the actions to handle the fault
  E.g., fetch the page from origin/remote, fix up PTE, …
Followers piggyback on the leader’s work
W
R
R
0xbeef
Fault stage

## Slide 35: Outline
Compiler/toolchain support for multi-ISA binaries
OS support for heterogeneous migration
Evaluation, ongoing and future work
Conclusion

## Slide 36: Evaluation
36
Workload sets drawn from HPC benchmark suite (NPB)
E5-1650 & APM XGENE
Popcorn yields 30% energy savings on average (max is 66% for set-3)
Popcorn yields 11% reduction in energy-delay product
66% gain!
30%
11%

## Slide 37: Preliminary result NPB EP
Chart: Cores x Nodes
| 4x1 | 4x2 | 4x3 | 4x4
Class B | 57.74 | 29.7 | 19.98 | 15.21
Class C | 231.21 | 118.08 | 79.97 | 61.19

## Slide 38: Ongoing and future work
Popcorn Linux extension to PowerPC64
Popcorn Xen: unikernels migration across ISAs
  Unikernels are minimalist statically compiled guests VMs
    Application + libraries + thin OS layer
    Simpler to migrate across ISA than regular VM
    Leverage the HermitCore unikernel and the KVM migration infrastructure
http://www.hermitcore.org/

## Slide 39: Outline
Compiler/toolchain support for multi-ISA binaries
OS support for heterogeneous migration
Evaluation, ongoing and future work
Conclusion

## Slide 40: Conclusion
Multiple OS-capable ISAs present in the datacenter
  Each one with pros and cons
Popcorn infrastructure allows to reap the benefits from these ISAs by having them cooperate
  To leverage ISA/Machine affinity, and perform smart consolidation/load balancing
  Tools and mechanisms: heterogeneous compiler + distributed OS + DSM
    Application and thread migration/distribution across ISAs
Unmodified applications enables high programmability: POSIX/shared memory run as-is

## Slide 41: Thank you
popcornlinux.org
ssrg.ece.vt.edu

## Slide 42: Backup slides - compiler

## Slide 43: The Case for Heterogeneous-ISA Multicore
43
“Harnessing ISA Diversity: Design of a Heterogeneous-ISA Chip Multiprocessor,” A. Venkat and D. M. Tullsen, ISCA 2014.
Single thread performance for different area budgets
Core Area (mm2)
Smaller the core area, greater # of cores can be placed on the silicon
ARM’s thumb
x86_64
Alpha
big Alpha
medium Alpha
little Alpha
Alpha
Performance of bzip2's two different phases for different peak power budgets
Phase 1
Phase 2

## Slide 44: Fine-Grained Migration
Can only migrate at equivalence points
  Scheduler must wait for thread to reach equivalence point
Perform addition & update pointers
Perform addition
Update pointers
Notes: Compiler implements program logic using features of each ISA
In this example:
  ARMv8 has extremely flexible memory access capabilities, updates array pointers while performing addition
  x86 doesn’t mix math with memory address generation, compiler generates addition and pointer updates in separate instructions
  Green line denotes equivalence point

## Slide 45: Fine-Grained Migration
DBT Framework
Previous idea: use dynamic binary translation (DBT) to emulate up until equivalence point [Venkat’15]
x86-64 Code
Scheduler
Thread
Migrate to ARM
ARM64 Code
Thread
Reached equivalence point
Notes: Downsides
  Expensive – need to lift assembly to IR and then code-gen
    May take a while to warm up code cache
    Contention on emulator data structures in multithreaded scenarios
  Code bloat – either put DBT framework in kernel (increase attack surface), or tie DBT into each application

## Slide 46: Fine-Grained Migration
New Idea: use hardware transactional memory to roll back to most recently encountered equivalence point
x86-64 Code
ARM64 Code
Scheduler
Migrate to ARM
cache
HTM buffer
Thread
. .. .
. .
Roll back to previous equivalence point
Thread
Notes: Hardware transactional memory
  Used for concurrency control, basically implements checkpointing in HW
As threads execute, start checkpointing at equivalence point
  When we reach the next equivalence point, commit results & start new checkpoint
Downsides
  Processors must implement HTM (Intel x86 TSX, Power8 HTM)
  Limitations in buffer sizes (4MB read, 22KB write on Intel; 8KB read, 8KB write buffer on Power8)

## Slide 47: Work-Sharing Across Processors
OpenMP runtime currently only executes threads on single architecture
Idea: launch threads across multiple processors, split parallel work across available resources
Multi-core
Many-core
OpenMP Work
Notes: Work splitting across devices well studied in CPU/GPU literature
  Programmability issues, limitations in kernel complexity, developer oftentimes has to help split data
Build new OpenMP runtime for smart load balancing across architectures
  Use messaging layer to transparently migrate data
  Runtime should dynamically adapt load across architectures
    Load balance based on capabilities
    Smart mapping of threads/customized data layout to prevent false sharing & page “ping-pong”

## Slide 48: Extensions to New ISAs
Popcorn currently supports ARM64/x86-64

## Slide 49: Extensions to New ISAs
Extend to new platforms, i.e., POWER8, SPARC
  Different performance/power/cost design points
Idea: build “compiler-compiler” to automatically generate support for new architecture
Compiler-compiler
LLVM Module
State Transform Module

## Slide 50: Backup slides – OS support

## Slide 51: Memory consistency protocol In reality …
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Origin
Remote 1
Remote 2
Write
Read
Write
Write
Read
R
Write
Invalidate
Write
RW
Read
Read
Write
Write

## Slide 52: Tracking ongoing fault handling
Track outstanding fault handlings
Stage ongoing fault handlings on “fault stage”
Coalesce similar type of faults if possible
  <Local read> + local reads
  <Local write> + local writes
  Otherwise, wait until the ongoing fault is handled or retry
A leader handle the fault on behalf of other followers
Notes:   <Local write> + local read
  <Local read> + remote reads
  <Remote read> + local reads
  …